## Slide 1
Dual enthalpy economizer, demand-control ventilation (DCV), and variable frequency drive (VFD) control
(7) Onboard sensors for occupancy, temperature, light, humidity, sound, CO2 & optional particulate matter
(8) Relays
(4) Analog outputs
(8) Universal Inputs
BACnet and Modbus control
75F® HyperStat Split
Advanced Rooftop Controls Over Two Wires
SPEC SHEET
Standard 18/2 Thermostat Wire
724-276-3035 | Support@Airoverse.com | Airoverse.com
1

## Slide 2
The HyperStat Split empowers contractors to upgrade rooftop units with Advanced Rooftop Control with unprecedented ease, bringing energy efficiency to more buildings than ever before. Using only two existing wires from the RTU to the thermostat, the HyperStat Split provides dual enthalpy economizer, demand-control ventilation, and VFD control. An onboard PIR occupancy sensor enhances energy savings with auto away, and its hefty I/O package enables alerts like condensate overflow and dirty filters.
OVERVIEW
The HyperStat Split facilitates ARC over the existing two wires in retrofit applications using a HyperLite and a Connect Module. Both an occupant interface and a powerful indoor air quality sensing station, the HyperLite takes user input and collects data on temperature, humidity, light, sound, CO2, occupancy, and particulate matter. The Connect Module communicates with the HyperLite over two wires from the RTU or FCU and performs stage or modular control. With the ability to accept eight universal analog inputs, the back half of the Connect Module moves load control away from the zone.
KEY FEATURES
Dual enthalpy economizer, demand-control ventilation, and VFD control for full Advanced Rooftop Controls over two wires
Condensate overflow and dirty filter sensors with notifications for advanced alerts
Real-time access to sensor data and remote control over building parameters through Facilisight, 75F’s building intelligence suite of web and mobile apps
Secure and proprietary encrypted 900 MHz wireless mesh network allows for lightweight, reliable communications between devices, eliminating the need to run wires throughout a space
ADDITIONAL FEATURES
Over-the-air firmware updates
Works over the two wires provided for the thermistor to report temperature to the RTU
Plug-and-Play solution for Advanced Rooftop Control
EQUIPMENT CONTROL
Up to three stages of cooling/heating/fan or fully modulating:
Rooftop Units
Unit Heaters
75F® HyperStat Split
2
724-276-3035 | Support@Airoverse.com | Airoverse.com
INCLUDED
(1) Mounting Adapter Plate
(2) Mounting Screws
(1) Each of HyperLite and Connect Module

## Slide 3
165mm
115mm
113mm
112mm
113mm
155mm
29mm
75F® HyperLite
MECHANICAL
SENSORS
ELECTRICAL
COMMUNICATIONS
Dimensions
Mounting
Screen
Operating Range
Temperature
Humidity
Light
Sound
Occupancy
PM2.5, PM10
Power
Bluetooth
Mesh
Wired
6.5” x 4.5” x 1.15” (165mm x 115mm x 29 mm)
(2) screws in drywall
2.8” 240x320 pixel TFT LCD
-4°F to 122°F (-20°C to 50°C)
Operating range between -4°F to 122°F (-20°C to 50°C); typical accuracy of +/- 1°F or 0.2°C
Operating range between 20 to 85% noncondensing; Typical accuracy of +/- 2% RH
Ambient light sensor; high-accuracy UV index sensor; matches erythemal curve; < 100 mix resolution
40-120dB response for 100 Hz to 10Khz
Passive Infra Red (PIR) with detection
range of 4m with 30-degree angle
Detection range of
0-1000ug/m3 and accuracy of +/-
10ug/m3 (PM2.5, 0-100 ug/m3) or
+/- 25ug/m3 (PM10, 0-100ug/m3)
24V AC/DC (+/-15%) with nominal
power consumption 1.0W and maximum consumption of 2.5W
BLE4.1; used during commissioning
900 MHz IEEE 802.15.4-compliant; used for device communication on mesh network
4 wire RS-485 interface
3 wire connector for low-power sensor bus
Dedicated
CO2 Sensor
Range 0-40’000 ppm; Accuracy +/-30ppm over range of 400-10,000ppm and lifetime of 15 years
OPTIONAL SENSORS
3
724-276-3035 | Support@Airoverse.com | Airoverse.com

## Slide 4
724-276-3035 | Support@Airoverse.com | Airoverse.com
MECHANICAL
ELECTRICAL
COMMUNICATIONS
Dimensions
Mounting
Screen
Power
Bluetooth
Wired
24V AC/DC (+/-15%) with nominal
power consumption 1.0W and maximum consumption of 2.5W
Bluetooth – Available for future use.
Modbus RTU / BACnet over RS485 communication
Sensor bus
Power over RS485 to enable communication with the HyperLite and power the unit over standard thermostat wires.
Dedicated Modbus/BACnet MSTP ports to interface with 3rd party BMS devices.
I/O
Inputs
Outputs
(8) Universal inputs.
(1) Sensor Bus
(4) 0-10V dc or 4-20mA analog outputs
(8) relays rated at 1A, 120V ac or 24 V ac/dc resistive load
5.5” x 4.13” x 1.22” (140 mm x 105 mm x 31mm)
Wall
TFT LCD, 1.77", 128(RGB)* 160 Pixels
140
105
31
75F® Connect Module
4